## Slide 1: OLYMPEX Ground Instruments
Joe Zagrodnik

## Slide 2: Olympic Peninsula Overview
Legend
= WSR-88D
= NPOL
= DOW
= EC X-Band
= MRR = SNOTEL
= Ground Obs sites
= Snow camera network = UW Tipping bucket network
= Chehalis rain gauge network
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 3: Ground Sites--Windward side of Olympics/Quinault Valley

## Slide 4: UW Tipping Bucket Network
*Data logging only, no data transmission
Locations:
Notes: Some may be replaced with NASA’s dual tipping buckets to gain real-time data. However, vandalism is a known issue with sites on the north shore ridges

## Slide 5
Name | Elev | Instruments X = currently deployed, P = Planned, U = Possible/Under Discussion |  |  |  |  |  |  |  | Power | Access
 |  | MRR | PIP | 2DVD | Parsivel | Pluvio | Hot Plate | Dual Tipping Gauge | Other |  | 
Lee Side |  |  |  |  |  |  |  |  |  |  | 
Hurricane Ridge | 5140’ | X | X |  | X |  | X |  |  | Yes | Road, Winter Conditions
Windward side (Quinault Valley region) |  |  |  |  |  |  |  |  |  |  | 
Wallace Cabin | Sea level | U |  | U | P |  |  |  | X= Tip Gauge | Yes | Road
Seed Orchard | 255’ |  |  |  | P |  |  | P |  | No | Road
Fish Hatchery | 170’ | P |  | P | X |  |  | X |  | Yes | Road
Amanda Park | 290’ |  |  | P |  |  |  | P |  | Yes | Road
Norwood South Shore Road | 220’ |  |  | U | P |  |  | P |  | Maybe | Road
Bunch Field | 380’ |  |  |  | U |  |  | P | X | No | Road, short walk
CRN Site | 285’ | P |  | P | P |  |  |  |  | Yes | Road
Graves Creek Campground | 563’ |  |  |  | P | U |  | P |  | No | Road and Trail
Neilton Pt | 2156’ | U | U | P | P | P | U |  |  | Yes | Road, Winter Conditions
Enchanted Valley | 2033’ |  |  |  | P | P |  |  |  | No | Trail
Wynoochee Trailer | 3160’ |  |  |  | X | X |  |  |  | No | Road, winter conditions, trail
Notes: Explain format of table without details—go over sites, instruments, and power/access (by color)
----- Meeting Notes (1/20/15 15:22) -----
Change P* to something else`

## Slide 6
Name | Elev | Instruments X = currently deployed, P = Planned, U = Possible/Under Discussion |  |  |  |  |  |  |  | Power | Access
 |  | MRR | PIP | 2DVD | Parsivel | Pluvio | Hot Plate | Dual Tipping Gauge | Other |  | 
Lee Side |  |  |  |  |  |  |  |  |  |  | 
Hurricane Ridge | 5140’ | X | X |  | X |  | X |  |  | Yes | Road, Winter Conditions
Windward side (Quinault Valley region) |  |  |  |  |  |  |  |  |  |  | 
Wallace Cabin | Sea level | U |  | U | P |  |  |  | X= Tip Gauge | Yes | Road
Seed Orchard | 255’ |  |  |  | P |  |  | P |  | No | Road
Fish Hatchery | 170’ | P |  | P | X |  |  | X |  | Yes | Road
Amanda Park | 290’ |  |  | P |  |  |  | P |  | Yes | Road
Norwood South Shore Road | 220’ |  |  | U | P |  |  | P |  | Maybe | Road
Bunch Field | 380’ |  |  |  | U |  |  | P | X | No | Road, short walk
CRN Site | 285’ | P |  | P | P |  |  |  |  | Yes | Road
Graves Creek Campground | 563’ |  |  |  | P | U |  | P |  | No | Road and Trail
Neilton Pt | 2156’ | U | U | P | P | P | U |  |  | Yes | Road, Winter Conditions
Enchanted Valley | 2033’ |  |  |  | P | P |  |  |  | No | Trail
Wynoochee Trailer | 3160’ |  |  |  | X | X |  |  |  | No | Road, winter conditions, trail
Notes: Move Pluvio
----- Meeting Notes (1/20/15 15:29) -----
U for under discussion
Take P* off of MRR Wallace Cabin, set on Neilton Pt

## Slide 7: Low Elevation with Power
Data recording/transmission:
  Cell coverage
Accessibility:
  Paved roads
Maintenance:
  Monitor via cell network
  Service when needed
  Swap gauge platform batteries every 4-6 weeks
Fish Hatchery
Notes: Remove instrument listing (mention instruments on previous slide)

## Slide 8
Name | Elev | Instruments X = currently deployed, P = Planned, U = Possible/Under Discussion |  |  |  |  |  |  |  | Power | Access
 |  | MRR | PIP | 2DVD | Parsivel | Pluvio | Hot Plate | Dual Tipping Gauge | Other |  | 
Lee Side |  |  |  |  |  |  |  |  |  |  | 
Hurricane Ridge | 5140’ | X | X |  | X |  | X |  |  | Yes | Road, Winter Conditions
Windward side (Quinault Valley region) |  |  |  |  |  |  |  |  |  |  | 
Wallace Cabin | Sea level | U |  | U | P |  |  |  | X= Tip Gauge | Yes | Road
Seed Orchard | 255’ |  |  |  | P | P |  | P |  | No | Road
Fish Hatchery | 170’ | P |  | P | X |  |  | X |  | Yes | Road
Amanda Park | 290’ |  |  | P |  |  |  | P |  | Yes | Road
Norwood South Shore Road | 220’ |  |  | U | P |  |  | P |  | Maybe | Road
Bunch Field | 380’ |  |  |  | U |  |  | P | X | No | Road, short walk
CRN Site | 285’ | P |  | P | P |  |  |  |  | Yes | Road
Graves Creek Campground | 563’ |  |  |  | P | U |  | P |  | No | Road and Trail
Neilton Pt | 2156’ | U | U | P | P |  | U |  |  | Yes | Road, Winter Conditions
Enchanted Valley | 2033’ |  |  |  | P | P |  |  |  | No | Trail
Wynoochee Trailer | 3160’ |  |  |  | X | X |  |  |  | No | Road, winter conditions, trail

## Slide 9: Low Elevation, No Power
Powered by solar panel + 1-2 batteries
Data transmission/recording:
  Cell (where available)
Accessibility:
  Road, short trails
Maintenance:
  Swap batteries
  Empty Pluvio after 16” of precip (or major event)
Bunch Field

## Slide 10
Name | Elev | Instruments X = currently deployed, P = Planned, U = Possible/Under Discussion |  |  |  |  |  |  |  | Power | Access
 |  | MRR | PIP | 2DVD | Parsivel | Pluvio | Hot Plate | Dual Tipping Gauge | Other |  | 
Lee Side |  |  |  |  |  |  |  |  |  |  | 
Hurricane Ridge | 5140’ | X | X |  | X |  | X |  |  | Yes | Road, Winter Conditions
Windward side (Quinault Valley region) |  |  |  |  |  |  |  |  |  |  | 
Wallace Cabin | Sea level | U |  | U | P |  |  |  | X= Tip Gauge | Yes | Road
Seed Orchard | 255’ |  |  |  | P |  |  | P |  | No | Road
Fish Hatchery | 170’ | P |  | P | X |  |  | X |  | Yes | Road
Amanda Park | 290’ |  |  | P |  |  |  | P |  | Yes | Road
Norwood South Shore Road | 220’ |  |  | U | P |  |  | P |  | Maybe | Road
Bunch Field | 380’ |  |  |  | U |  |  | P | X | No | Road, short walk
CRN Site | 285’ | P |  | P | P |  |  |  |  | Yes | Road
Graves Creek Campground | 563’ |  |  |  | P | U |  | P |  | No | Road and Trail
Neilton Pt | 2156’ | U | U | P | P | P | U |  |  | Yes | Road, Winter Conditions
Enchanted Valley | 2033’ |  |  |  | P | P |  |  |  | No | Trail
Wynoochee Trailer | 3160’ |  |  |  | X | X |  |  |  | No | Road, winter conditions, trail

## Slide 11: High Elevation with Power
Data recording/transmission:
  Cell coverage
Accessibility:
  6-mile dirt road (Neilton Pt.)
  Winter conditions (blowdowns, snow, mudslides)
Maintenance:
  Monitor via cell network
  Snow/rime removal
  Empty Pluvio after 16” of precip (or major event)
Neilton Pt.

## Slide 12
Name | Elev | Instruments X = currently deployed, P = Planned, U = Possible/Under Discussion |  |  |  |  |  |  |  | Power | Access
 |  | MRR | PIP | 2DVD | Parsivel | Pluvio | Hot Plate | Dual Tipping Gauge | Other |  | 
Lee Side |  |  |  |  |  |  |  |  |  |  | 
Hurricane Ridge | 5140’ | X | X |  | X |  | X |  |  | Yes | Road, Winter Conditions
Windward side (Quinault Valley region) |  |  |  |  |  |  |  |  |  |  | 
Wallace Cabin | Sea level | U |  | U | P |  |  |  | X= Tip Gauge | Yes | Road
Seed Orchard | 255’ |  |  |  | P |  |  | P |  | No | Road
Fish Hatchery | 170’ | P |  | P | X |  |  | X |  | Yes | Road
Amanda Park | 290’ |  |  | P |  |  |  | P |  | Yes | Road
Norwood South Shore Road | 220’ |  |  | U | P |  |  | P |  | Maybe | Road
Bunch Field | 380’ |  |  |  | U |  |  | P | X | No | Road, short walk
CRN Site | 285’ | P |  | P | P |  |  |  |  | Yes | Road
Graves Creek Campground | 563’ |  |  |  | P | U |  | P |  | No | Road and Trail
Neilton Pt | 2156’ | U | U | P | P | P | U |  |  | Yes | Road, Winter Conditions
Enchanted Valley | 2033’ |  |  |  | P | P |  |  |  | No | Trail
Wynoochee Trailer | 3160’ |  |  |  | X | X |  |  |  | No | Road, winter conditions, trail
Notes: Talk about spectrum of capability/utility—from yellow to purple say how they gradually become less capable/more difficult

## Slide 13: High Elevation, No Power
Powered by solar panel + 8 deep cycle batteries
Data recording/transmission:
  No cell coverage
Accessibility:
  Enchanted Valley:
    13-mile backcountry trail
  Wynoochee
    7-mile unmaintained gated road
    Winter conditions (deep snow, blowdowns, mudslides)
Maintenance:
  Visit every 2-3 weeks
  Snow/rime removal
  Empty Pluvio
  Recharge batteries if insufficient solar
Wynoochee
Notes: Enchanted valley—hiking is only option, mules likely needed for deployment
Wynoochee—road poorly marked, likely blocked by blowdowns and/or mudslides

## Slide 14: 2014-2015 Test Results
  Trailer simulating high elevation, no power
  Currently located at Snoqualmie Pass (Elev: 3,000’) in Cascades
  8 deep-cycle batteries + solar panel
  Parsivel, Pluvio
  Real time monitoring
  via cell network

## Slide 15: Snoqualmie Pass Trailer Battery
(Set of 8 batteries + solar panel)
Sunny periods
Notes: Point out downward trend…trailer is in favorable location, Olympics are more cloudy

## Slide 16: Heavy Precip. Event Jan 4-5, 2015
Missing data
Snow Mix Rain

## Slide 17: Hurricane Ridge

## Slide 18
Name | Elev | Instruments X = currently deployed, P = Planned, U = Possible/Under Discussion |  |  |  |  |  |  |  | Power | Access
 |  | MRR | PIP | 2DVD | Parsivel | Pluvio | Hot Plate | Dual Tipping Gauge | Other |  | 
Lee Side |  |  |  |  |  |  |  |  |  |  | 
Hurricane Ridge | 5140’ | X | X |  | X |  | X |  |  | Yes | Road, Winter Conditions
Windward side (Quinault Valley region) |  |  |  |  |  |  |  |  |  |  | 
Wallace Cabin | Sea level | U |  | U | P |  |  |  | X= Tip Gauge | Yes | Road
Seed Orchard | 255’ |  |  |  | P |  |  | P |  | No | Road
Fish Hatchery | 170’ | P |  | P | X |  |  | X |  | Yes | Road
Amanda Park | 290’ |  |  | P |  |  |  | P |  | Yes | Road
Norwood South Shore Road | 220’ |  |  | U | P |  |  | P |  | Maybe | Road
Bunch Field | 380’ |  |  |  | U |  |  | P | X | No | Road, short walk
CRN Site | 285’ | P |  | P | P |  |  |  |  | Yes | Road
Graves Creek Campground | 563’ |  |  |  | P | U |  | P |  | No | Road and Trail
Neilton Pt | 2156’ | U | U | P | P | P | U |  |  | Yes | Road, Winter Conditions
Enchanted Valley | 2033’ |  |  |  | P | P |  |  |  | No | Trail
Wynoochee Trailer | 3160’ |  |  |  | X | X |  |  |  | No | Road, winter conditions, trail

## Slide 19: Hurricane Ridge
Data recording/transmission:
  Cell coverage
Accessibility:
  17-mile paved road, maintained weekends only
  4+ hour drive from NPOL
Maintenance:
  Snow/rime removal
  PIP alignment/bulb replacement
Notes: Example: PIP bulb burned out

## Slide 20: Wind Observations

## Slide 21: Management Needs
Type | # Sites | Visit Frequency | Data Retrieval | Access Issues
Low elevation with power | 4 | 4-6 weeks, as needed | Cell | -
Low elevation, no power | 4 | 1-2 weeks, as needed | Site dependent | Mudslides
High elevation with Power* | 2 | 1-2 weeks, as needed | Cell | Snow, road closures
High Elevation, no power | 2 | 1-2 weeks, as needed | ? | No vehicle access
*Includes Hurricane Ridge
Notes: *As needed is very important—after a major 10-15” rainstorm, all Pluvios will have to be emptied
*It is expected that snow/rime removal and heavier precip rates will require higher elevation sites to be visited more frequently

## Slide 22: Extra Slides

## Slide 23: Accessibility
US-101
Paved Road
Maintained Dirt Road
Unmaintained Dirt Road
13-mile backcountry trail
Unmaintained after Oct-1
Mudslides likely
Snow, mudslides possible